## Slide 1: EECE 2160 Collision Detection Algorithm Improvement
Jamin Eisenberg

## Slide 2: Project Overview
Used the DE1-SoC board’s VGA port to display free-moving and rotating shapes that could bounce off each other
Breakdown
  Read from the keypad
  Write to the VGA port and the speaker
  Produce a system to represent any polygon on-screen
  Implement an IEEE algorithm for collision detection
  Improve that algorithm
  Make the shapes interact with each other
  Evaluate the algorithms
4 weeks

## Slide 3: Polygon System
Polygons contain
  Lines which contain
    Vectors which contain
      X and Y coordinates
CollisionPairs contain 2 Polygons that are colliding
  Can resolve the collision

## Slide 4: Original Algorithm
AABBs: two points that define the limits of a shape
For each shape called i
  For each shape called j
    If i is the same as j, they’re not colliding
    If i and j are colliding, make a CollisionPair with them
i and j are colliding if
  The x distance between the shapes is less than half their combined width
  OR the same thing with y distance and height
Slow!

## Slide 5: Improved Algorithm
Sorting makes everything faster
Problem can be separated in 2
  X collisions
  Y collisions
  If shapes are colliding in x and y, they’re colliding
Shapes can be reduced to “intervals”
For every shape’s interval
  If the interval is the start of the shape
    It’s colliding with all the currently active intervals
    Add it to the list of active intervals
  Otherwise
    Remove the start of this interval from the active list
Fast!

## Slide 6: Algorithm Comparison
My improved algorithm is faster than the original in every case
236x faster in the case of 100 Xs
Chart: Original vs Improved Algorithm for Squares
| 1 | 10 | 100 | 200
Original | 0.13367 | 1.5795 | 90.6606 | 195.187
Improved | 0.050607 | 0.11043 | 2.9735 | 9.1521
Chart: Original vs Improved Algorithm for Xs
| 1 | 10 | 100 | 200
Original | 0.24155 | 12.4653 | 577.627 | 1336.33
Improved | 0.03655 | 0.20209 | 2.4456 | 11.396

## Slide 7: Issue 1: Memory Mapping
Delay: 5 days (non-intensive)
Tried to access the physical addresses of the machine to write to the VGA port
  Got segmentation fault
Reviewed memory mapping
Mapped the physical memory to virtual memory and read and wrote to there

## Slide 8: Issue 2: Set Intersection
Delay: 2 days
Sets in C++ are ordered, so we need a way to order its elements
All the sets were of CollisionPairs
How do you order elements that contain two other elements?
  Lexicographically
operator< override wasn’t working, so a struct was made

## Slide 9: Issue 3: Collision Handling
Delay: ongoing
Collision handling works sometimes and I can’t tell what differentiates the cases where it works and where it doesn’t
My approach:
  Calculate relative positions and velocities between 2 shapes
  Calculate the x and y overlap of the two shapes
  If the x overlap is greater, resolve the collision in the y direction
  Otherwise, resolve in the x direction
  To resolve the collision:
    Calculate the collision normal, then the relative velocity in the normal’s direction
    If that’s negative, don’t resolve
    Change the shapes’ velocities according to their mass relative to the total mass

## Slide 10: Demo

## Slide 11: EECE 2160 Collision Detection Algorithm Improvement
Jamin Eisenberg